## Slide 1: RL Cooperative Transportation using fixed-wings drones
RL Project
Part of thesis

## Slide 2: Residual MARL
Action Space: δ𝑓 ∈ R3n
  Keep wrench controller and optimizer. Run decentralized
  𝑓 (𝑡) = 𝑓𝑔(𝑡)+ 𝑓𝜆(𝑡) + δ𝑓(t)
  Much better learning when decomposed
  𝑓 (𝑡) = G(t)† · (wd(t) + δw(t)) + N(t) · (λ(t) + δλ(t))
  δw ∈ R6 , δλ ∈ Rn

## Slide 3: Residual MARL
Observation Space (Original) ∈ R44 :
  Measured load state ∈ R18
  [pL(t), RL(t), L(t), ωL(t)]
  Own carrier position and velocity ∈ R6
  [pR(t), (t)]
  Base force components
  [𝑓𝑔(𝑡), 𝑓𝜆(𝑡)]
  Fourier time embedding/features
    ϕ(t) = [sin(ω1​t),cos(ω1​t),sin(ω2​t),cos(ω2​t),… sin(ωkt), cos(ωkt)]

## Slide 4: Residual MARL
Observation Space (Augmented) ∈ R98 :
Original Observation Space in addition to:
  The last two measured load states ∈ R24
  [pL(t-1), RL(t-1), L(t-1), ωL(t-1)]
  [pL(t-2), RL(t-2), L(t-2), ωL(t-2)]
  The last two own carrier position and velocity ∈ R12
  [pR(t-1), (t-1)]
  [pR(t-2), (t-2)]
  Reference load state at current time ∈ R18
  [pLd(t), RLd(t), Ld(t), ωLd(t)]
Did not lead to an improvement

## Slide 5: Residual MARL
Critic state ∈ R58
  True load state ∈ R18
  [pL(t), RL(t), L(t), ωL(t)]
  All carriers’ positions ∈ R12
  [pR1(t), pR2(t), pR3(t), pR4(t)]
  All carriers’ velocities ∈ R12
  [(t), (t), (t), (t)]
  Expert-generated carrier position ∈ R12
  [pRe1(t), pRe2(t), pRe3(t), pRe4(t)]
  Delay of each carrier load measurement ∈ R4
  [d1,d2,d3,d4]
Notes: Preferire un carattere sans serif come Arial, Helvetica o Verdana. Font consigliabile da 30 a 40 pt.
Allineare i testi a sinistra, non giustificarli.
Utilizzare non più di tre blocchi di informazione di massimo 2/3 righe ciascuno.
Per evidenziare titoli o parole chiave, prediligere l’uso del grassetto a corsivo o colori.
Prediligere testo nero su sfondo bianco.
Evitare ombre, sfumature e gradazioni di grigio.
Secondo le linee guida sull’accessibilità, prestare attenzione ai contrasti tra i colori di sfondo e il testo.

## Slide 6: Residual MARL
Reward function
  Design Methodology: Start simple and add terms by observing failure modes
  Per drone reward is:
  Team reward:
Notes: Preferire un carattere sans serif come Arial, Helvetica o Verdana. Font consigliabile da 30 a 40 pt.
Allineare i testi a sinistra, non giustificarli.
Utilizzare non più di tre blocchi di informazione di massimo 2/3 righe ciascuno.
Per evidenziare titoli o parole chiave, prediligere l’uso del grassetto a corsivo o colori.
Prediligere testo nero su sfondo bianco.
Evitare ombre, sfumature e gradazioni di grigio.
Secondo le linee guida sull’accessibilità, prestare attenzione ai contrasti tra i colori di sfondo e il testo.

## Slide 7: Residual MARL
Reward function terms breakdown:
  Truncation Condition: A one-shot penalty of −100 is triggered on a guard-truncated step if speed exceeds vblowup = 100.
Term | Expression | Role
manifold (di2) | ‖pexpert,i(t) − pi(t)‖² | Stay on the expert loiter loop. The goal is not to follow it exactly, but to learn the underlying orbiting behavior in general.
stalli | Graced hinge below cruise floor: d² + 1.0 · d, where d = max(0, (ε + margin) − ‖vi‖) | Fixed-wing stall floor (prevents airspeed drop)
load tracking | ‖eL‖² | Keep the load on reference
overspeedi2 | min(over² + 2 · over, 75) where over = max(0.0, vi − overspeed_v) | Prevent carrier from speeding up unnecessarily. Blowup guardrail.
overshooti | min(overλ,i² + overλ,i ,9) where overλ,i = max(0, satλ,i − 1) and satλ,i = ‖δλi‖₂ / (κλ · ‖λi,base‖₂) κλ: the allowable fraction of the base controller magnitude | Prevents the policy from taking actions above the allowed fraction of the base controller magnitude (dead gradient, no learning). The cap prevents the policy from taking overly aggressive actions.
Term | Expression | Role
manifold (di2) | ‖pexpert,i(t) − pi(t)‖² | Stay on the expert loiter loop. The goal is not to follow it exactly, but to learn the underlying orbiting behavior in general.
stalli | Graced hinge below cruise floor: d² + 1.0 · d, where d = max(0, (ε + margin) − ‖vi‖) | Fixed-wing stall floor (prevents airspeed drop)
 | ‖eL‖² | Keep the load on reference
overspeedi2 | min(over² + 2 · over, 75) where over = max(0.0, vi − overspeed_v) | Prevent carrier from speeding up unnecessarily. Blowup guardrail.
overshooti | min(overλ,i² + overλ,i ,9) where overλ,i = max(0, satλ,i − 1) and satλ,i = ‖δλi‖₂ / (κλ · ‖λi,base‖₂) κλ: the allowable fraction of the base controller magnitude | Prevents the policy from taking actions above the allowed fraction of the base controller magnitude (dead gradient, no learning). The cap prevents the policy from taking overly aggressive actions.
Notes: Preferire un carattere sans serif come Arial, Helvetica o Verdana. Font consigliabile da 30 a 40 pt.
Allineare i testi a sinistra, non giustificarli.
Utilizzare non più di tre blocchi di informazione di massimo 2/3 righe ciascuno.
Per evidenziare titoli o parole chiave, prediligere l’uso del grassetto a corsivo o colori.
Prediligere testo nero su sfondo bianco.
Evitare ombre, sfumature e gradazioni di grigio.
Secondo le linee guida sull’accessibilità, prestare attenzione ai contrasti tra i colori di sfondo e il testo.

## Slide 8: Residual MARL: Some Results
Notes: Preferire un carattere sans serif come Arial, Helvetica o Verdana. Font consigliabile da 30 a 40 pt.
Allineare i testi a sinistra, non giustificarli.
Utilizzare non più di tre blocchi di informazione di massimo 2/3 righe ciascuno.
Per evidenziare titoli o parole chiave, prediligere l’uso del grassetto a corsivo o colori.
Prediligere testo nero su sfondo bianco.
Evitare ombre, sfumature e gradazioni di grigio.
Secondo le linee guida sull’accessibilità, prestare attenzione ai contrasti tra i colori di sfondo e il testo.

## Slide 15: Università degli Studi di Padova