## Slide 1
Reward Terms Summary
Term | Expression | Role
manifold (d2) | ‖p_expert,i(t) − p_i‖² (time-indexed, phase-correct) | Stay on the expert loiter loop — served by dλ
stall | Graced hinge below cruise floor: d² + 1.0 · d, where d = max(0, (ε + margin) − ‖v_i‖) (first 20 steps skipped) | Fixed-wing stall floor (prevents airspeed drop)
load track (load_err2) | ‖e_p‖² (load position error, global) | Keep the load on reference — served by dwrench
overspeed (over2) | Clipped hinge above v_overspeed = 3.0: min(over² + 2 · over, 75) | Shear/blowup guardrail — penalty for load-invisible modes
λ-overshoot (oshoot) | Clipped hinge on sat_λ − 1: min(os² + 1.0 · os, 9), where os = max(0, sat_λ − 1) | Un-freezes the dλ dead-zone (bites only above cap, zero below → full authority is free)
Terminal Condition: A one-shot penalty of −100 is triggered on a guard-truncated step if speed exceeds v_blowup = 100.